## Slide 1
Steel surface defect classification
Source: Industrial_Defect_Detection.ipynb
01
NEU benchmark · six defect types · grayscale texture images
The task
Classify each 200 × 200 steel image into one of six defect categories.
1,800
images · 300 per class
Why transfer learning
Only 1,260 images train the model. ImageNet pretraining supplies reusable visual filters, while fine-tuning adapts them to steel textures.
Benchmark design
Compare a small CNN trained from scratch with ResNet-50 and EfficientNet-B0. This tests whether pretrained features improve accuracy on a small, balanced dataset.
Notes: Dataset facts and the notebook rationale. The notebook reports 1,800 grayscale 200×200 images, six classes with 300 images each, and describes both ResNet-50 and EfficientNet-B0 as ImageNet-pretrained transfer-learning approaches.

## Slide 2
Preprocessing and useful visual cues
Source: Industrial_Defect_Detection.ipynb
02
Input preparation
Grayscale → 3-channel RGB → resize to 224 × 224 → ImageNet normalization
Training augmentation
Flips, 90° turns, affine shifts/rotations, CLAHE, brightness/contrast changes and noise broaden the small training set.
Why these steps
CLAHE can expose faint contrast; geometric and photometric changes reduce sensitivity to orientation, position and lighting. Validation/test used resize + normalization only.
What the network learned
Grad-CAM highlights defect regions. The notebook interprets these cues as:
Edges and lines
scratches
Fine texture networks
crazing
Local intensity anomalies
inclusions
All six classes had 300 images; no resampling or class weighting was needed for this benchmark.
Notes: Preprocessing and augmentation follow cells 4–5 and the dataset class-count output. Grad-CAM output is qualitative evidence; edge/texture/intensity interpretations come from the notebook summary and should not be read as a feature-importance ranking.

## Slide 3
EfficientNet-B0 ties for accuracy with a smaller footprint
Source: Industrial_Defect_Detection.ipynb
03
Test accuracy (%)
Chart: 
| Baseline CNN | ResNet-50 | EfficientNet-B0
Test accuracy | 68.15 | 99.63 | 99.63
MODEL
ACCURACY / MACRO F1
PARAMETERS
Baseline CNN
68.15% / 68.53%
0.36M
ResNet-50
99.63% / 99.63%
24.03M
EfficientNet-B0
99.63% / 99.63%
4.02M
Same test score as ResNet-50 with about 6× fewer parameters; the notebook reports 0.55 ms/image versus 0.70 ms/image on its test setup.
Best practical choice in this comparison: EfficientNet-B0.
Notes: Model comparison values are copied from the notebook’s test-set comparison table. Latency depends on the notebook hardware and timing method; it is not a deployment guarantee. Parameter ratio: 24.03M / 4.02M ≈ 6.0.

## Slide 4
Evaluation: strong holdout result, one observed error
Source: Industrial_Defect_Detection.ipynb
04
Split and metrics
Stratified split: 70% train (1,260) · 15% validation (270) · 15% test (270)
Primary comparison: macro F1; also accuracy, macro precision/recall, per-class report and confusion matrix.
EfficientNet-B0 on test set
99.63%
accuracy · 99.63% macro F1
269 / 270 correct
Observed error
One true scratch was classified as an inclusion (86.0% predicted confidence; 9.3% probability assigned to the true class).
Per-class recall
100% for four classes; 97.78% for scratches; 100% for inclusion. Inclusion precision was 97.83%.
Notes: The notebook uses stratified 70/15/15 splits with random_state=42. The 270-image test set has 45 examples per class. EfficientNet-B0 made one error: scratches → inclusion. Macro F1 and precision/recall are reported.

## Slide 5
Limits and next steps
Source: Industrial_Defect_Detection.ipynb
05
Result
EfficientNet-B0 separates the six NEU classes very well on one stratified holdout set.
What remains uncertain
Small, balanced, single-source dataset; one fixed split; no external plant/domain test. The six-image demo does not establish generalization. High accuracy may not transfer to new mills, cameras or defect severity.
Stronger evidence
1 Test on a separate mill, camera or production lot; split by source/lot to avoid near-duplicate leakage.
2 Repeat with cross-validation and report confidence intervals plus per-class error counts.
3 Add difficult and rare examples; evaluate calibration and an abstain/review threshold.
4 For deployment, benchmark end-to-end latency and extend from image classification to defect localization if operators need defect position.
Next milestone: validate on a separate production source.
Notes: Limitations and recommendations are framed as next experiments rather than measured notebook outcomes. The notebook tests one fixed 270-image holdout from NEU and reports a six-image demo; those data do not establish production performance.